## Slide 1
Digital Electronics (303105220)
Alpita makwana, Assistant Professor
Mechatronics Engineering

## Slide 2
Sequential Circuits
CHAPTER-4
A 1-bit memory, the circuit properties of Bi-stable latch, the clocked SR flip flop, J- K-T and D types flip flops, applications of flip flops, shift registers, applications of shift registers, ring counter, sequence generator, ripple (Asynchronous) counters, synchronous counters, special counter IC’s, asynchronous sequential counters, applications of counters.

## Slide 3
Sequential Circuits
Sequential circuits are digital circuits that store and use the previous state information to determine their next state.
Unlike combinational circuits, which only depend on the current input values to produce outputs, sequential circuits depend on both the current inputs and the previous state stored in memory elements.
Sequential circuits are commonly used in digital systems to implement state machines, timers, counters, and memory elements.
The memory elements in sequential circuits can be implemented using flip-flops, which are circuits that store binary values and maintain their state even when the inputs change.

## Slide 4
Flip-flop: Another name for bistable multivibrator. Used for storing a single bit (memory element)
Sequential Circuits
FF
Normal output
Inverted output
Inputs
State of FF: State of Q
State of FF:
High/1/SET , for Q=1
Low/0/RESET, for Q=0
The inputs cause change in output state (Flip-Flop)
FF input is applied temporarily to change its output state.
Input applied in form of pulses.
The output now remains in new state, even when input is removed (Memory)
Used to store 1-bit of data.
Basic component of shift-registers and counters.
*Non-clocked FF is called Latch
Latch: Level-triggered
FF: Edge-triggered

## Slide 5
Sequential Circuits
A Flip Flop is a memory element that is capable of storing one bit of information.
It is also called as a Bistable Multivibrator since it has two stable states either 0 or 1.

## Slide 6
Sequential Circuits
Using NOR gates
Using NAND gates

## Slide 7
Bistable Latch/RS Flip-flop: Circuit properties
Sequential Circuits
Case I:
Case II:
NAND-GATES

## Slide 8
Bistable Latch/RS Flip-flop: Circuit Properties
Sequential Circuits
The outputs and are always complementary.
The circuits has two stable states. One state is (Set state),
Another is (Reset state).
The circuits continues to be in the same state, zero or one.
How to store the desired bit ?
Used to enter desired bit
NOR-GATES

## Slide 9
Sequential Circuits
Case I: |  | Input to G1 |  |  | Input to G2 | Output of G2 (
 | 0 | 1,0 | 1 | 0 | 1,1 | 0
Case II: |  | Input to G1 |  |  | Input to G2 | Output of G2 (
 | 0 | 1,1 | 0 | 0 | 1,0 | 1
 |  | Input to G1 |  |  | Input to G2 | 
 | 0 | 1,0 | 1 | 0 | 1,1 | 0
 |  | Input to G1 |  |  | Input to G2 | 
 | 0 | 1,1 | 0 | 0 | 1,0 | 1
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 10
Sequential Circuits
Case I: |  | Input to G1 |  |  | Input to G2 | Output of G2 (
 | 1 | 0,0 | 1 | 0 | 1,1 | 0
Case II: |  | Input to G1 |  |  | Input to G2 | Output of G2 (
 | 1 | 0,1 | 1 | 0 | 1,1 | 0
 |  | Input to G1 |  |  | Input to G2 | 
 | 1 | 0,0 | 1 | 0 | 1,1 | 0
 |  | Input to G1 |  |  | Input to G2 | 
 | 1 | 0,1 | 1 | 0 | 1,1 | 0
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 11
Sequential Circuits
 |  |  |  | Remarks
0 | 0 |  |  | No change
0 | 1 | 0 | 1 | reset condition
1 | 0 | 1 | 0 | set condition
1 | 1 | Not valid | Not valid | Invalid combination
 |  |  |  | Remarks
0 | 0 |  |  | No change
0 | 1 | 0 | 1 | reset condition
1 | 0 | 1 | 0 | set condition
1 | 1 | Not valid | Not valid | Invalid combination
SR | 00 | 01 | 11 | 10
0 |  |  | X | 1
1 | 1 |  | X | 1
 | 00 | 01 | 11 | 10
0 |  |  | X | 1
1 | 1 |  | X | 1
Characteristic eq. of SR-FF:
NAND
NOR

## Slide 12
Sequential Circuits
Inputs |  |  | Output Q | Operation
Clock (CK) | Clear (Cr) | Preset (Pr) | Q | 
1 | 1 | 1 | Qn+1 | Normal FF
0 | 0 | 1 | 0 | Clear
0 | 1 | 0 | 1 | Preset
Clocked RS flip flop

## Slide 13
Sequential Circuits
 |  |  |  | Remarks
………………………. |  |  |  | 
1 | 1 | Not valid | Not valid | Invalid combination
 |  |  |  | Remarks
………………………. |  |  |  | 
1 | 1 | Not valid | Not valid | Invalid combination
JK- flip flop
Data inputs |  | Outputs |  | Inputs to SR FF |  | Output
0 | 0 | 0 | 1 | 0 | 0 | 0 (=)
0 | 0 | 1 | 0 | 0 | 0 | 1 (=)
1 | 0 | 0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 1 (=)
1 | 1 | 1 | 0 | 0 | 1 | 0 (=)
Data inputs |  | Outputs |  | Inputs to SR FF |  | 
0 | 0 | 0 | 1 | 0 | 0 | 
0 | 0 | 1 | 0 | 0 | 0 | 
1 | 0 | 0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 
1 | 1 | 1 | 0 | 0 | 1 | 
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 14
Sequential Circuits
JK- flip flop
Inputs |  | Output
0 | 0 | 
0 | 1 | 0
1 | 0 | 1
1 | 1 | 
Inputs |  | Output
0 | 0 | 
0 | 1 | 0
1 | 0 | 1
1 | 1 | 
 | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 1
 | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 1

## Slide 15
Sequential Circuits
Race-around condition
Inputs |  | Output
0 | 0 | 
0 | 1 | 0
1 | 0 | 1
1 | 1 | 
Inputs |  | Output
0 | 0 | 
0 | 1 | 0
1 | 0 | 1
1 | 1 | 
Leading (positive) edge
Trailing (negative) edge
Output oscillates after every when the clock pulse () is high,
when both JK inputs are high.
At the end of clock pulse, the output is not certain.
Avoided, if is made smaller than . Practical method - use Master Slave flip flop
The propagation delay through two NAND gates in series.

## Slide 16
Sequential Circuits
Master-Slave Flip-flop (Pulse triggered FF)
The Race-around Condition can be avoided by ensuring that the clock input is at logic “1” only for a very short time.
The Master-Slave Flip-Flop is a combination of two JK flip-flops connected in a series configuration.
One acts as the “master” and the other as a “slave”.
The output from the master flip-flop is connected to the two inputs of the slave flip flop whose output is fed back to the inputs of the master flip-flop.
In addition to these two flip-flops, the circuit also includes an inverter.
The inverter is connected to the clock pulse in such a way that the inverted clock pulse is given to the slave flip-flop. In other words if CLK=0 for a master flip-flop, then CLK=1 for a slave flip-flop, and if CLK=1 for a master flip flop then it becomes 0 for a slave flip-flop.

## Slide 17
Sequential Circuits
Master-Slave Flip-flop (Pulse triggered FF)

## Slide 18
Sequential Circuits
D (Delay) flip flop
Inputs |  | Output
0 | 0 | 
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
Inputs |  | Output
0 | 0 | 
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
 | 0 | 1
0 | 0 | 1
1 | 0 | 1
 | 0 | 1
0 | 0 | 1
1 | 0 | 1
Characteristic Table of D-FF

## Slide 19
Sequential Circuits
D flip flop: From SR flip flop
S
R
0 | 0 | 0 | 0 | X
0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 1 | X | 0
0 | 0 | 0 | 0 | X
0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 1 | X | 0
Characteristic Table
of D-FF
Excitation table
of SR-FF
 | 0 | 1
0 | 0 | 1
1 | 0 | X
 | 0 | 1
0 | 0 | 1
1 | 0 | X
 | 0 | 1
0 | X | 0
1 | 1 | 0
 | 0 | 1
0 | X | 0
1 | 1 | 0

## Slide 20
Sequential Circuits
D flip flop: From JK flip flop
J
K
0 | 0 | 0 | 0 | X
0 | 1 | 0 | X | 1
1 | 0 | 1 | 1 | X
1 | 1 | 1 | X | 0
0 | 0 | 0 | 0 | X
0 | 1 | 0 | X | 1
1 | 0 | 1 | 1 | X
1 | 1 | 1 | X | 0
Characteristic Table
of D-FF
Excitation table
of JK-FF
 | 0 | 1
0 | 0 | 1
1 | X | X
 | 0 | 1
0 | 0 | 1
1 | X | X
 | 0 | 1
0 | X | X
1 | 1 | 0
 | 0 | 1
0 | X | X
1 | 1 | 0

## Slide 21
Sequential Circuits
T (Toggle) flip flop
Inputs |  | Output
0 | 0 | 
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Inputs |  | Output
0 | 0 | 
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
 | 0 | 1
0 | 0 | 1
1 | 1 | 0
 | 0 | 1
0 | 0 | 1
1 | 1 | 0
Characteristic Table of T-FF

## Slide 22
Sequential Circuits
T flip flop: From JK flip flop
0 | 0 | 0 | 0 | X
0 | 1 | 1 | X | 0
1 | 0 | 1 | 1 | X
1 | 1 | 0 | X | 1
0 | 0 | 0 | 0 | X
0 | 1 | 1 | X | 0
1 | 0 | 1 | 1 | X
1 | 1 | 0 | X | 1
Characteristic Table
of T-FF
Excitation table
of JK-FF
 | 0 | 1
0 | 0 | 1
1 | X | X
 | 0 | 1
0 | 0 | 1
1 | X | X
 | 0 | 1
0 | X | X
1 | 0 | 1
 | 0 | 1
0 | X | X
1 | 0 | 1

## Slide 23
Sequential Circuits
Excitation Tables of FFs:
Flip-flop conversion

## Slide 24
Sequential Circuits
Timing diagrams of FFs:
Q: Consider the following Clock and Input waveforms to the FF.
Sketch the output waveforms for the following FFs:
Positive-edge triggered D-type FF 74 AHC74.
Positive-level triggered D-type FF 7475.
Negative-edge triggered JK-Flip flop 74HC112.

## Slide 25
Sequential Circuits
Positive-edge
Negative-edge
Positive-level

## Slide 26
Sequential Circuits
(Positive-edge
Triggered)
(Positive-level
Triggered)
(Negative-edge
triggered)

## Slide 27
Sequential Circuits
Applications of flip flop:
Frequency dividers
Counters
Storage registers
Shift registers
Data storage
Bounce elimination switch
Latch
Data transfer
Memory
Registers

## Slide 28
Sequential Circuits
Shift Registers:
A Register is a device that is used to store such information.
Intel's 8085 processor contains many 8-bit registers for storage and result purposes,
It is a group of flip-flops connected in series used to store multiple bits of data. The information stored within these registers can be transferred with the help of shift registers.
Shift Register is a group of flip flops used to store multiple bits of data. The bits stored in such registers can be made to move within the registers and in/out of the registers by applying clock pulses.
An n-bit shift register can be formed by connecting n flip-flops, where each flip-flop stores a single bit of data.
The registers which will shift the bits to the left are called Shift-left registers. The registers which will shift the bits to the right are called Shift-right registers

## Slide 29
Sequential Circuits
Data can be entered and retrieved in following forms:
Serial-In Serial-out
Serial-in Parallel-out
Parallel-in serial-out
Parallel-in parallel-out
A 3-bit shift-register using 7474 positive-edge triggered FF

## Slide 30
Sequential Circuits

## Slide 31
Sequential Circuits
Shift Register Application - Ring Counter:
Typical application of the Shift register.
The output of the last flip-flop is connected to the input of the first flip-flop in the case of the ring counter but in the case of the shift register it is taken as output.
Except for this, all the other things are the same.
Overriding Input
Clock (-ve
Edge-Triggered)

## Slide 32
Sequential Circuits
The clock pulse (CLK) is simultaneously applied to all the flip-flops. (Synchronous Counter)
Also, here we use Overriding input (ORI) for each flip-flop - Preset (PR) and Clear (CLR) are used as ORI.
When PR is 0, then the output is 1, and when CLR is 0, then the output is 0.
PR and CLR are active low signals that always work in value 0.
PR = 0, Q = 1; CLR= 0, Q = 0

## Slide 33
Sequential Circuits
ORI is connected to Preset (PR) in FF-0 and it is connected to Clear (CLR) in FF-1, FF-2, and FF-3.
Output Q = 1 is generated at FF-0, and the rest of the flip-flop generates output Q = 0.
This output Q = 1 at FF-0 is known as Preset 1, which is used to form the ring in the Ring Counter.
ORI | CLK | Q0 | Q1 | Q2 | Q3
0 | X | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0 | 0
Counter states (modulo-n)
Preset 1

## Slide 34
Sequential Circuits
Johnson’s counter
Counts 2*n states (modulo-2n)
ORI | CLK | Q0 | Q1 | Q2 | Q3
0 | X | 1 | 0 | 0 | 0
1 | 0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0
Counter states

## Slide 35
Sequential Circuits
STRAIGHT RING COUNTER | TWISTED RING COUNTER
It connects the output of the last shift register to the input of first shift register. | It connects the complement of output of the last shift register to the input of the first register.
It is known as One hot counter. | It is known as Walking ring counter or Johnson’s counter.
Number of states = number of flip-flops | Number of states = 2 x number of flip-flops
It circulates a single bit (0 or 1) around the ring. | It circulates stream of 1 followed by stream of 0.
PRESET is used in first shift register. | PRESET is not used in twisted ring counter.
CLEAR is used for last (n-1) flip-flops. | CLEAR is used for all flip-flips in it.
It is used in successive approximation and stepper motor control. | It is used in phase shift or function generator.

## Slide 36
Sequential Circuits
Shift registers are also utilized in Sequence generator circuits
Sequence generator: generates a given sequence of bits (in synchronism with a clock)
The minimum no. of FFs (N) required to generate a sequence of length S-

## Slide 37
Sequential Circuits
Q: Generate a sequence …1101011…
The minimum no. of FFs (N) required to generate a sequence of length 7: . So,
No. of clock pulses | Flip-flop outputs |  | 
1 | 1 | 1 | 1
2 | 1 | 1 | 1
3 | 0 | 1 | 1
4 | 1 | 0 | 1
5 | 0 | 1 | 0
6 | 1 | 0 | 1
7 | 1 | 1 | 0
. | . | . | .
. | . | . | .
No. of clock pulses | Flip-flop outputs |  | 
1 | 1 | 1 | 1
2 | 1 | 1 | 1
3 | 0 | 1 | 1
4 | 1 | 0 | 1
5 | 0 | 1 | 0
6 | 1 | 0 | 1
7 | 1 | 1 | 0
. | . | . | .
. | . | . | .
Same states

## Slide 38
Sequential Circuits
Q: Generate a sequence …1101011…
No. of clock pulses | Flip-flop outputs |  |  |  | Serial input Y
 |  |  |  |  | Serial input Y
1 | 1 | 1 | 1 | 0 | 1
2 | 1 | 1 | 1 | 1 | 0
3 | 0 | 1 | 1 | 1 | 1
4 | 1 | 0 | 1 | 1 | 0
5 | 0 | 1 | 0 | 1 | 1
6 | 1 | 0 | 1 | 0 | 1
7 | 1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 | 0 | 1
2 | 1 | 1 | 1 | 1 | 0
3 | 0 | 1 | 1 | 1 | 1
No. of clock pulses | Flip-flop outputs |  |  |  | Serial input Y
 |  |  |  |  | Serial input Y
1 | 1 | 1 | 1 | 0 | 1
2 | 1 | 1 | 1 | 1 | 0
3 | 0 | 1 | 1 | 1 | 1
4 | 1 | 0 | 1 | 1 | 0
5 | 0 | 1 | 0 | 1 | 1
6 | 1 | 0 | 1 | 0 | 1
7 | 1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 | 0 | 1
2 | 1 | 1 | 1 | 1 | 0
3 | 0 | 1 | 1 | 1 | 1
  Diff. states

## Slide 39
Sequential Circuits
Q: Generate a sequence …1101011…
 | 00 | 01 | 11 | 10
00 | X | X | X | X
01 | X | 1 | 1 | X
11 | X | 1 | 0 | 0
10 | X | X | 1 | 1
 | 00 | 01 | 11 | 10
00 | X | X | X | X
01 | X | 1 | 1 | X
11 | X | 1 | 0 | 0
10 | X | X | 1 | 1

## Slide 40
Sequential Circuits
Counters:
Asynchronous (ripple counter): All FFs not clocked simultaneously
Synchronous (Ring: modulo-n, Twisted ring: modulo-2n) counter: All FFs clocked simultaneously
Counter state | Count |  | 
0 | 0 | 0 | 0
1 | 0 | 0 | 1
2 | 0 | 1 | 0
3 | 0 | 1 | 1
4 | 1 | 0 | 0
5 | 1 | 0 | 1
6 | 1 | 1 | 0
7 | 1 | 1 | 1
Counter state | Count |  | 
0 | 0 | 0 | 0
1 | 0 | 0 | 1
2 | 0 | 1 | 0
3 | 0 | 1 | 1
4 | 1 | 0 | 0
5 | 1 | 0 | 1
6 | 1 | 1 | 0
7 | 1 | 1 | 1
However, total possible states with n-FFs:
) counter is possible
changes from 0 to 1
changes from 1 to 0, changes from 0 to 1
changes from 1 to 0, changes from 1 to 0,
changes from 0 to 1
changes with every clock pulse
changes with every 2-clock pulses
changes with every 4-clock pulses
up-counter & down-counter
up-counter

## Slide 41
Sequential Circuits
Design Procedure:
Q0 needs to change with every clock pulse.
So, the input to FF0 is T0=1, and the external clock is provided to FF0.
Q1 toggles when Q0 goes from 1 to 0.
It means that the Negative edge of Q0 toggles Q1. So we can use Q0 as the clock input for FF1.
Q2 toggles when Q1 goes from 1 to 0 (negative edge).
This is used as a clock signal for FF2.
A 3-bit binary counter

## Slide 42
Sequential Circuits
0
0
0
0
1
0
0
0
1
1
1
0
1
0
0
1
1
0
1
0
1
1
1
1
0
0
0

## Slide 43
Sequential Circuits
Q. Design a mod-5 synchronous up counter using J-K flip flop
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
Desired states
0 | 0 | 0 | X
0 | 1 | 1 | X
1 | 0 | X | 1
1 | 1 | X | 0
0 | 0 | 0 | X
0 | 1 | 1 | X
1 | 0 | X | 1
1 | 1 | X | 0
Excitation table of JK FF

## Slide 44
Sequential Circuits
Q. Design a mod-5 synchronous up counter using J-K flip flop
Desired states
Present state |  |  | Next state |  |  | Flip flop inputs |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 1 | 0 | X | 0 | X | 1 | X
0 | 0 | 1 | 0 | 1 | 0 | 0 | X | 1 | X | X | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | X | X | 0 | 1 | X
0 | 1 | 1 | 1 | 0 | 0 | 1 | X | X | 1 | X | 1
1 | 0 | 0 | 0 | 0 | 0 | X | 1 | 0 | X | 0 | X
1 | 0 | 1 | X | X | X | X | X | X | X | X | X
1 | 1 | 0 | X | X | X | X | X | X | X | X | X
1 | 1 | 1 | X | X | X | X | X | X | X | X | X
Present state |  |  | Next state |  |  | Flip flop inputs |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 1 | 0 | X | 0 | X | 1 | X
0 | 0 | 1 | 0 | 1 | 0 | 0 | X | 1 | X | X | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | X | X | 0 | 1 | X
0 | 1 | 1 | 1 | 0 | 0 | 1 | X | X | 1 | X | 1
1 | 0 | 0 | 0 | 0 | 0 | X | 1 | 0 | X | 0 | X
1 | 0 | 1 | X | X | X | X | X | X | X | X | X
1 | 1 | 0 | X | X | X | X | X | X | X | X | X
1 | 1 | 1 | X | X | X | X | X | X | X | X | X
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
Excitation table for mod-5 counter

## Slide 45
Sequential Circuits
 | 00 | 01 | 11 | 10
0 | 0 | 0 | x | x
1 | 0 | 1 | x | x
 | 00 | 01 | 11 | 10
0 | 0 | 0 | x | x
1 | 0 | 1 | x | x
 | 00 | 01 | 11 | 10
0 | x | x | x | 1
1 | x | x | x | x
 | 00 | 01 | 11 | 10
0 | x | x | x | 1
1 | x | x | x | x
 | 00 | 01 | 11 | 10
0 | 0 | x | x | 0
1 | 1 | x | x | x
 | 00 | 01 | 11 | 10
0 | 0 | x | x | 0
1 | 1 | x | x | x
 | 00 | 01 | 11 | 10
0 | x | 0 | 1 | x
1 | x | x | x | x
 | 00 | 01 | 11 | 10
0 | x | 0 | 1 | x
1 | x | x | x | x
 | 00 | 01 | 11 | 10
0 | 1 | 1 | x | 0
1 | x | x | x | x
 | 00 | 01 | 11 | 10
0 | 1 | 1 | x | 0
1 | x | x | x | x
 | 00 | 01 | 11 | 10
0 | x | x | x | x
1 | 1 | 1 | x | x
 | 00 | 01 | 11 | 10
0 | x | x | x | x
1 | 1 | 1 | x | x

## Slide 46
Sequential Circuits
Logic “1”
CLK
mod-5 synchronous up-counter using J-K flip flop

## Slide 47
Sequential Circuits
Special counter ICs:
74HC161
74HC163
74HC191
74HC160
CD4017B
Applications of counters:
Pulse counting
Frequency division
Digital clocks
Analog-to-digital converters